## Slide 1: A Guide to OpenFlow Test-bed Setup
Jian Li
Supervisor: Prof. Jae Hyoung Yoo
Division of IT Convergence Engineering
POSTECH, Korea
gunine@postech.ac.kr
2013. 09. 17

## Slide 2: Outline
Introduction
Installation Procedures
  Mininet Installation
  Floodlight Installation
Tutorial
  Mininet Tutorial
  Floodlight Tutorial
Demo
  Demo scenarios
  Demo execution procedures

## Slide 3: Introduction (1/2)
OpenFlow
  A communication protocol that gives access to the data plane of a network switch or router over the network
OpenFlow Enabling Technologies
  Mininet
    A network emulator runs a collection of end-hosts, switches, routers, and links on a single Linux kernel
  Open vSwitch (OVS)
    An open-source virtual switch software designed for virtual servers
    Forward traffic between different virtual hosts within same physical host
    Support OpenFlow 1.0 ~ 1.2, and 1.3 is work in progress
  Floodlight
    A completely open, free, Java-based OpenFlow controller
    Include Southbound and Northbound API which implemented in Java
    The latest version of Floodlight implements OpenFlow v1.0
      OpenFlow v1.0 is implemented using Java included inside Floodlight source
Notes: In routing, the forwarding plane, sometimes called the data plane, defines the part of the router architecture that decides what to do with packets arriving on an inbound interface. Most commonly, it refers to a table in which the router looks up the destination address of the incoming packet and retrieves the information necessary to determine the path from the receiving element, through the internal forwarding fabric of the router, and to the proper outgoing interface(s). The IP Multimedia Subsystem architecture uses the term transport plane to describe a function roughly equivalent to the routing control plane.

## Slide 4: Introduction (2/2)
Floodlight Controller
Java App
Jython App
OVS Switch
OVS Switch
OVS Switch
OVS Switch
Static Flow Pusher
REST- based App
Southbound API
Northbound API
OVS Switch
Host
Host
Host
Host
Host
Host
Host
Host
Host
Host
mininet
Implement OpenFlow Protocol
Not standardized yet, use proprietary APIs

## Slide 5: Mininet Installation (1/2)
Mininet VM Installation
  The most easiest and most foolproof way of installing Mininet
  Procedures
    Download the Mininet pre-installed VM image
    Download and install one of the hypervisors (e.g., VirtualBox, Qemu, VMware Workstation, VMware Fusion, or KVM)
    Import VM image into selected hypervisor
Native Installation from Source
  Recommended OS: Ubuntu 11.10 and later
  Procedures
    Download source from github
    Run installation script Full installation will install everything that is included in the Mininet VM, such as Open vSwitch as well the additions like the OpenFlow wireshark and controller Minimal installation will install only dependency package of Mininet and Open vSwitch
$ git clone git://github.com/mininet/mininet
$ mininet/util/install.sh -a
$ mininet/util/install.sh -fnv
full
minimal

## Slide 6: Mininet Installation (2/2)
Native Installation from Package
  Recommended OS: Ubuntu 12.04 and later
  Procedures
    Remove all previously installed Mininet and Open vSwitch
    Install Mininet package according to your Ubuntu version (choose one of them!)
    Deactive OpenvSwitch controller if it is running
    You can also install additional software from mininet source
$ sudo rm -rf /usr/local/bin/mn /usr/local/bin/mnexec \
/usr/local/lib/python*/*/*mininet* \
/usr/local/bin/ovs-* /usr/local/sbin/ovs-*
$ sudo apt-get install mininet
$ sudo apt-get install mininet/quantal-backports
$ sudo apt-get install mininet/precise-backports
Ubuntu 13.04
Ubuntu 12.10
Ubuntu 12.04
$ sudo service openvswitch-controller stop
$ sudo update-rc.d openvswitch-controller disable
$ git clone git://github.com/mininet/mininet
$ mininet/util/install.sh -fw

## Slide 7: Floodlight Installation
Native Install from Source
  Procedures
    Install pre-requisite software packages
    Download source from github and build the stable version
    Run the floodlight
    Dash board access through web browser
$ sudo apt-get install openjdk-7-jdk
$ sudo apt-get install ant
# yum install java-1.7.0-openjdk java-1.7.0-openjdk-devel
# yum install ant
Ubuntu
EPEL (CentOS)
$ git clone git://github.com/floodlight/floodlight.git
$ cd floodlight
$ git checkout stable
$ ant
# ./foodlight.sh
http://<controller_ip>:8080/ui/index.html

## Slide 8: Mininet Tutorial (1/3)
Mininet Command Line Interface (CLI) Usage
  Interact with hosts and switches
    Start a minimal topology
    Start a minimal topology using a remote controller
    Start a custom topology
    Display nodes
    Display links
    Dump information about all nodes
    Check the IP address of a certain node
    Print the process list from a host process
$ sudo mn
mininet> nodes
mininet> net
mininet> dump
mininet> h1 ifconfig -a
mininet> h1 ps -a
$ sudo mn --controller=remote, ip=[controller IP], port=[ctrl listening port]
$ sudo mn --custom [topo_script_path] --topo [topo_name]

## Slide 9: Mininet Tutorial (2/3)
Mininet CLI Usage
  Test connectivity between hosts
    Verify the connectivity by pinging from host0 to host1
    Verify the connectivity between all hosts
  Run a regression test
    Traffic receive preparation
    Traffic generation from client
  Link variations
  Python Interpreter
    Print accessible local variables
    Execute a method through invoking mininet API
mininet> h1 ping -c 1 h2
mininet> pingall
$ sudo mn -link tc,bw=[bandwidth],delay=[delay_in_millisecond]
mininet> iperf -s -u -p [port_num] &
mininet> iperf -c [IP] -u -t [duration] -b [bandwidth] -p [port_num] &
$ py locals()
$ py [mininet_name_space].[method]

## Slide 10: Mininet Tutorial (3/3)
Mininet Application Programming Interface (API) Usage
  mininet.node.Node
    A shell interface for obtain/assign information from/to a certain node
  mininet.topo.Topo
    Data center network representation for structured multi-trees
Class | Method | Description
Topo | addHost | Add a host to topology, get dictionary type as second parameter for specifying detailed options such as IP, MAC and etc.
 | addSwitch | Add a switch to topology, switch has no IP/MAC, identified by DPID
 | addLink | Link two nodes into together
 | addNode | Add a node to topology
 | addPort | Generate port mapping for new edge
 | switches | Return all switches
 | hosts | Return all hosts
Node | MAC/setMAC | Return/Assign MAC address of a node or specific interface
 | IP/setIP | Return/Assign IP address of a node or specific interface
 | cmd | Send a command, wait for output, and return it
 | terminate | Send kill signal to Node and clean up after it

## Slide 11: Floodlight Overview (1/2)
Floodlight Architecture
  Floodlight controller
  Application built as Java modules, application built over the REST API
Floodlight Controller
Module Manager
Thread Pool
Packet Streamer
Jython Sever
Web UI
Unit Tests
Device Manager
Topology Service
Link Discovery
Flow Cache
Storage
OpenFlow Services
Counter Store
Switches
Controller Memory
PerfMon
Trace
Java API
Memory
NoSQL
Module Applications
VNF
Firewall
StaticFlow EntryPusher
PortDown Reconciliation
Forwarding
Hub
Learning Switch
REST Applications
Circuit Pusher (python)
OpenStackQuantum Plugin (python)
Your Applications … 
REST API (Implement Restlet Routable Interface)
Notes: Circuit Pusher utilizes floodlight rest APIs to create a bidirectional circuit, i.e., permanent flow entry, on all switches in route between two devices based on IP addresses with specified priority.
FloodlightProvider
  Tracks switch add/removes
  Translate OpenFlow messages to Floodlight events
LinkDiscoveryManager
  Responsible for discovering and maintaining the status of links
TopologyService
  Maintains the topology information for the controller, and find routing in the network
ThreadPool
  A wrapper for a Java’s ScheduledExecutorService
  Can be used to have threads be run at specific times or periodically
Packet Streamer
  Can selectively stream Openflow packets exchanged between any switch and the controller to an observer

## Slide 12: Floodlight Overview (2/2)
Application Modules
  Forwarding: default reactive packet forwarding application
  Static Flow Entry Pusher
    Install specific flow entry (match + action) to a specific switch
  Firewall
    An application to apply ACL rules to allow/deny traffic based on specified match
  Port Down Reconciliation: reconcile flows across a network
  Virtual Network Filter (VNF)
    Simple MAC-based network isolation application
REST Applications
  The REST API is the recommended interface to develop applications utilizing Floodlight supported features
Core REST APIs
  Static Flow Pusher REST API
    Allow the user to proactively insert/delete/list the flows to OpenFlow switch
  Firewall REST API
    Allow the user to insert/delete/list rules for firewall

## Slide 13: Static Flow Pusher (1/2)
Definition
  A Floodlight module, exposed via REST API, that allows a user to manually insert flows into an OpenFlow switch
Reactive Flow Insertion (by Controller Automatically)
  A non-matched packet header is sent to the controller
  An appropriate flow is inserted based on the header information
Proactive Flow Insertion (by User Manually)
  Flows are inserted proactively to switches before packet arrive
OpenFlow Controller
host1
host2
switch1
switch2
query route
insert flows
SRC | DST | ACTION | …
SRC | DST | ACTION | …
h1_IP | h2_IP | port 2 | 
SRC | DST | ACTION | …
h1_IP | h2_IP | port 2 | 
SRC
…
DST
ETHER_TYPE
…
PAYLOAD
packet header
packet payload
Notes: Reactive Flow Insertion: 새로운 non-matched 패킷이 OpenFlow 스위치에 도착하여야만 새로운 Flow가 추가 되는 형태
Proactive Flow Insertion: 새로운 packet의 도달하기도 전에 사용자는 미리 특정 Flow를 OpenFlow Switch에 추가 할 수 있다.

## Slide 14: Static Flow Pusher (2/2)
Static Flow Pusher API
REST API Example
  Insert a flow on switch 1 (in  port 1, out  port 2)
  List all inserted flows
  Delete a static flow by its name ‘flow-mod-1’
curl -d '{"switch": "00:00:00:00:00:00:00:01", "name":"flow-mod-1", "cookie":"0",
"priority":"32768", "ingress-port":"1","active":"true", "actions":"output=2"}'
http://<controller_ip>:8080/.../json
curl http://<controller_ip>:8080/wm/core/switch/1/flow/json;
curl -X DELETE -d '{"name":"flow-mod-1"}' http://<controller_ip>:8080/wm/staticflowentrypusher/json
URI | Description | Arguments
/.../json | Add/delete static flow | HTTP POST data (add), HTTP DELETE (deletion)
/…/list/<switch>/json | List static flows | switch: Valid Switch DPID or "all"
/…/clear/<switch>/json | Clear static flows | switch: Valid Switch DPID or "all"

## Slide 15: DEMO Scenarios
Construct a Customized Topology Using Mininet
  A topology with two hosts and five switches (ovs) shown as below
Scenario #1
  Ping from host1 to host2 in reactive manner
Scenario #2
  Ping from host1 to host2 in proactive manner
    Choose route #1
    Choose route #2
host1
host2
switch1
switch2
switch4
Route #1
Route #2
switch3
switch5
1
2
3
1
2
1
2
1
2
1
2
3
0
0

## Slide 16: DEMO Execution Procedures
Procedures
  Start Floodlight controller daemon
  Initialize Mininet by specifying custom topology
  Initiate a ICMP request from host1
  Restart Mininet
  Insert flow entries into flow tables through Floodlight’s REST API
  Initiate a ICMP request from host1
# $FLOODLIGHT_PATH/floodlight.sh
$ sudo mn --custom ./topo.py --topo mytopo --controller=remote, ip=127.0.0.1
mininet> h1 ping h2
mininet> exit
$ sudo mn --custom ./topo.py --topo mytopo --controller=remote, ip=127.0.0.1
$ ./simpleTopoMod.sh route1/route2
mininet> h1 ping h2

## Slide 17: DEMO
DEMO

## Slide 18: Reference
[1] Mininet Installation, http://mininet.org/download/
[2] Mininet Python API Reference Manual, http://mininet.org/api/hierarchy.html
[3] Mininet Document, https://github.com/mininet/mininet/wiki/Documentation
[4] Floodlight Document, http://docs.projectfloodlight.org/display/floodlightcontroller
[5] OpenFlow Whitepaper, https://www.opennetworking.org/sdn-resources/sdn-library/whitepapers
[6] OpenFlow Spec 1.4.0, https://www.opennetworking.org/images/stories/downloads/sdn-resources/onf-specifications/openflow/openflow-spec-v1.4.0.pdf
[7] OpenvSwitch Document, http://openvswitch.org/support/
[8] Source Code for the DEMO, https://github.com/gunine/ITCE600

## Slide 19: Q&A

## Slide 20: Firewall REST API (1/2)
URI | Method | URI Arguments | Data | Description
/…/<op>/json | GET | op: status, enable, disable, storageRules, subnet-mask | None | query the status of, enable, and disable the firewall
/…/rules/json | GET | None | None | List all existing rules in json format
 | POST | None | {"<field 1>":"<value 1>", "<field 2>":"<value 2>", ...} Ex. "src-mac": "<xx:xx:xx:xx:xx:xx>" | Create new firewall rule "field":"value" pairs below in any order and combination:
 | DELETE | None | {"<ruleid>":"<int>"} | Delete a rule by ruleid
REST API Example
  Show whether the firewall is enabled or disabled
  Enable or Disable the firewall
curl http://localhost:8080/wm/firewall/module/status/json
curl http://localhost:8080/wm/firewall/module/enable/json
curl http://localhost:8080/wm/firewall/module/disable/json

## Slide 21: Firewall REST API (2/2)
REST API Example
  Adding an ALLOW rule for all flows to pass through switch 00:00:00:00:00:00:00:01
  Adding an ALLOW rule for all flows between IP host 10.0.0.3 and host 10.0.0.7 (default action is allow, no need to specify)
  Adding an ALLOW rule for UDP, and then block port 5010
curl -X POST -d '{"switchid": "00:00:00:00:00:00:00:01"}' http://localhost:8080/wm/firewall/rules/json
curl -X POST -d '{"src-ip": "10.0.0.3/32", "dst-ip": "10.0.0.7/32"}'
http://localhost:8080/wm/firewall/rules/json
curl -X POST -d '{"src-ip": "10.0.0.7/32", "dst-ip": "10.0.0.3/32"}'
http://localhost:8080/wm/firewall/rules/json
curl -X POST -d '{"src-ip": "10.0.0.3/32", "dst-ip": "10.0.0.7/32",
"nw-proto":"UDP" }' http://localhost:8080/wm/firewall/rules/json
curl -X POST -d '{"src-ip": "10.0.0.3/32", "dst-ip": "10.0.0.7/32",
"nw-proto":"UDP", "tp-src":"5010", "action":"DENY" }' http://.../rules/json